## Slide 1
Ⅰ. Introduction
■ Background
- It is necessary to develop In-situ measurement technology
that minimizes environmental impact and improves mobility.
■ Purpose
- In this research, the background spectrum was simulated
to reduce measurement uncertainty of the Peak to Compton
(PTC) method, which is an In-situ measurement technology
developed in previous research.
Background Spectrum Simulation for In-situ Measurement Technology
Byungchae Lee a, Seunggi Jeong a, Jihyun Yu a, Jonghoa Kim a, Jangsoo Suh a, Sangbum Hong b
a Sae-An Enertech Corporation, b Korea Atomic Energy Research Institute
■ Background Spectrum MCNP Simulation
- The background spectrum of the Compton continuum area
(381.38 to 410.29 keV) of 137Cs, a nuclide mainly emitted
from the contaminated site, was simulated by MCNP.
- Among the gamma rays emitted from natural nuclides, the
intensity was 1 % or more, and the energy spectra of 34
gamma rays affecting the 137Cs Compton continuum area
were simulated(Table 1).
- The Compton continuum area was calculated using the
ratio of the Full energy peak of the spectrum simulating
each gamma ray energy to the measured Full energy peak.
- The simulated background spectrum was compared with
39 spectra (28 in Daejeon and 11 in Jeju) measured in
an uncontaminated environment as shown in Fig. 1 to
evaluate the accuracy.
■ MCNP Geometry
- Detector : Potable High Purity Germanium detector
- Distance : 50cm
- Effective area : 1000cm ⅹ 1000cm
- Natural nuclides : Homogeneous at all depths
- Tally : F8
Ⅳ. Conclusions
■ In order to reduce the measurement uncertainty of the Peak
to Compton method, an In-situ measurement technology, the
background spectrum of the 137Cs Compton continuum area
was simulated with MCNP.
■ As a result of comparing the simulated background spectrum
with the spectrum measured in an uncontaminated
environment, the average relative error was within 5 %.
■ It is expected that this evaluation method will be able to
quickly and accurately evaluate radioactivity if it is applied to
the decommissioning site of a nuclear power plant or a site
contaminated by an accident in the future.
Ⅱ. Methods
Ⅲ. Results
■ Comparison by Region
- As a result of comparing the spectra measured in Daejeon
(No. 1 to 28) and Jeju (No. 29 to 39), it was found that
Jeju showed lower radioactivity.
- In the case of Jeju, it is judged that the radioactivity is
low because the proportion of natural nuclides contained
in the soil is lower than that of other regions.
■ Comparison of Measurement and MCNP
- Relative error : 0.01 ~ 4.81 %, High accuracy
- The reason for the high accuracy is considered to be
because the Full energy peak ratio of the measured and
simulated spectrum for each gamma ray energy was
calculated.
Nuclide | Energy (keV) | Intensity (%) | Nuclide | Energy (keV) | Intensity (%)
228Ac | 463.0 | 4.4 | 214Bi | 1155.2 | 1.6
7Be | 477.6 | 10.3 | 214Bi | 1238.1 | 5.8
208Tl | 511.0 | 22.6 | 214Bi | 1281.1 | 1.4
208Tl | 583.0 | 84.5 | 214Bi | 1377.7 | 4.0
214Bi | 609.3 | 46.1 | 214Bi | 1408.0 | 2.2
212Bi | 727.2 | 7.6 | 40K | 1460.8 | 11.0
214Bi | 768.4 | 4.9 | 214Bi | 1509.2 | 2.1
212Bi | 785.5 | 1.3 | 212Bi | 1620.6 | 1.5
228Ac | 794.7 | 4.3 | 228Ac | 1630.4 | 1.5
214Bi | 806.2 | 1.2 | 214Bi | 1661.3 | 1.2
56Mn | 846.8 | 98.9 | 214Bi | 1729.6 | 2.9
208Tl | 860.6 | 12.0 | 214Bi | 1764.5 | 15.4
228Ac | 911.1 | 25.8 | 214Bi | 1847.4 | 2.1
214Bi | 934.1 | 3.0 | 214Bi | 2118.6 | 1.1
228Ac | 964.4 | 5.0 | 214Bi | 2204.2 | 5.1
228Ac | 969.1 | 15.8 | 214Bi | 2447.9 | 1.6
214Bi | 1120.3 | 15.1 | 208Tl | 2614.7 | 99.0
Table 1. Gamma energy and intensity of natural nuclides.
Fig. 1. In-situ gamma-ray spectroscopy for
measurement of natural nuclides at sites.
Fig. 2. Gamma spectra of natural nuclides calculated by MCNP simulation
No | Measurement (CPS) | MCNP (Pulse) | Relative error (%) | No | Measurement (CPS) | MCNP (Pulse) | Relative error (%)
1 | 4.62 | 4.55 | 1.49 | 21 | 4.07 | 4.07 | 0.01
2 | 4.60 | 4.55 | 4.08 | 22 | 4.25 | 4.24 | 0.09
3 | 4.01 | 3.89 | 3.05 | 23 | 4.17 | 4.17 | 0.01
4 | 4.02 | 3.95 | 1.84 | 24 | 4.22 | 4.16 | 1.39
5 | 3.99 | 3.83 | 3.86 | 25 | 4.33 | 4.33 | 0.01
6 | 4.18 | 4.26 | 1.92 | 26 | 4.35 | 4.35 | 0.10
7 | 4.11 | 4.18 | 1.95 | 27 | 4.35 | 4.35 | 0.01
8 | 4.19 | 4.33 | 3.18 | 28 | 4.43 | 4.31 | 2.62
9 | 4.23 | 4.19 | 0.94 | 29 | 1.27 | 1.25 | 1.78
10 | 4.13 | 4.23 | 2.43 | 30 | 1.26 | 1.28 | 1.69
11 | 4.02 | 4.13 | 2.74 | 31 | 1.31 | 1.31 | 0.01
12 | 4.13 | 4.24 | 2.61 | 32 | 1.12 | 1.14 | 1.57
13 | 4.16 | 4.30 | 3.27 | 33 | 1.16 | 1.16 | 0.01
14 | 4.45 | 4.45 | 0.04 | 34 | 1.15 | 1.15 | 0.01
15 | 4.55 | 4.54 | 0.16 | 35 | 1.30 | 1.32 | 1.79
16 | 4.41 | 4.59 | 3.90 | 36 | 1.35 | 1.29 | 4.04
17 | 4.59 | 4.81 | 4.77 | 37 | 1.31 | 1.34 | 2.62
18 | 4.41 | 4.61 | 4.46 | 38 | 1.33 | 1.32 | 1.28
19 | 4.54 | 4.54 | 0.01 | 39 | 1.32 | 1.32 | 0.01
20 | 4.22 | 4.22 | 0.01 |  |  |  | 
Table 2. Comparison of In-situ measurement results and MCNP simulation results in 137Cs Compton
continuum area