## Slide 1
METHODS
RESULTS AND DISCUSSIONS
Acknowledge
Neutron Logging Sonde
  The method for configuring porosity
  or rock type of stratum
  Consisting of two neutron detectors
  (Near detector & Far detector)
  and one neutron source
3He Proportional Counter
  Gas proportional counter
  Increasing demands and cost of 3He
  Neutron Reaction
    3He(n, p)3H : ~ 940 barns (@ ~ 1 eV neutrons)
Stilbene Scintillator
  Neutron detection with PSD technique (Pulse Shape Discrimination)
  Neutron Reaction
    1H(n, n′)1H : ~ 1 barn (@ ~ 1 MeV neutrons)
This work was supported by Korea Environment Industry & Technology Institute (KEITI) through Subsurface Environment Management (SEM) Project, funded by Korea Ministry of Environment (MOE) (2018002440004).
Ill-hyuk Han, Geehyun Kim*
*Email : gk.rs@snu.ac.kr
Department of Nuclear Engineering, Seoul National University, 1, Gwanak-ro, Gwanak-gu, Seoul, Korea
A Comparison of Performance between
Stilbene and 3He Detectors for Neutron Sonde
Spring Meeting of the Korean Nuclear Society – ICC, Jeju, Korea, May 18-20, 2022
Monte Carlo Simulation (MCNP 6.2)
  Neutron Sonde design : Dual Neutron Probes of Robertson Geo.
  Formation of stratum : Radius = 5 m, Height = 12 m
INTRODUCTION
CONCLUSIONS
Stilbene can replace 3He detectors due to the following reasons
  Both detectors having a same tendency in the porosity calibration curves
  Higher neutron detection efficiency than 3He
The Far/Near Ratio of Stilbene scintillator is decreased due to increasing near detector counts, however, statistical error of the ratio is reduced
Simulation Variables | 
Detector | 3He tubes (or Stilbene scintillators)
Rock Type | Limestone, Granite, Sandstone, Basalt, Shale
Porosity | 0% – 100%
Temperature | 27°C
Neutron Source | 241Am-Be (1.1×107 n/s, 3 Ci)
Borehole Fluid | Water
Borehole Diameter | 14.0 cm – 22.0 cm
Shielding Material | Plastic(Polyethlene)
Fig. 1 Porosity calibration curve
of Neutron Sonde
Fig. 2 MCNP 6.2 simulation geometry
Table. 1 Variables of MCNP 6.2 simulation
Neutron Diffusion Equation
Borehole
Sonde Diameter
6.5 cm
Far Detector
2＂X 2＂
Air
Plastic
241Am-Be Source
SUS 409 housing
Water
Rock
Near Detector
2＂X 2＂
Slowing Down
  Subscript 1 : Fast Neutron
  Subscript 2 : Thermal Neutron
  D : Diffusion Coefficient
  Φ : Neutron Flux
  : Reaction Cross-section
  Q : Neutron Source’s Emission Rate
  𝐿1 : Slowing Down Length
  𝑟𝑓 : Distance from source to far detector
  𝑟𝑛 : Distance from source to near detector
Neutron Reaction Spectrum
  Simulations for Limestone with 0.1% porosity at 150 mm borehole
  3He tubes for near detectors
    Lower counts overall energy range due to gas phase detectors
    No detection for fast neutrons
    (E > 1 keV)
  Stilbene scintillators for near detectors
    Higher counts overall energy range due to solid state detectors
    Much more efficient for fast neutrons than 3He tubes
Fig. 3 Neutron counts of two neutron detectors by channels
(a) 3He proportional counters (b) Stilbene scintillators
Porosity Calibration Curve by Each Borehole Diameter
Fig. 5 Porosity calibration curves by each borehole diameters of two Neutron Sondes
Simulations for Limestone with 3He tubes and Stilbene scintillators
The borehole diameter proportional to the amount of water, resulting in the decrease of the Far/Near Ratio
(a)
(b)
Porosity Calibration Curve by Each Rock Type
Simulations at 150 mm borehole with 3He tubes and Stilbene scintillators
To both Neutron Sondes, no tendency to rock types except Shale which has lots of water
Stilbene showing the calibration curves shifted to the left compared with 3He
(a)
(b)
(a) 3He proportional counters (b) Stilbene scintillators
Fig. 4 Porosity calibration curves by each rock types of two Neutron Sondes
Reasons for the Reduced Far/Near Ratio by Stilbene Scintillator
More possible for fast neutrons to pass shielding materials between neutron source and near detector rather than thermal neutrons
Decreasing statistical error of the ratio by Stilbene scintillators due to higher neutron detection efficiency
Fig. 7 Near detector counts for
Limestone at 150 mm borehole
Thermal
Fast
Near Detector Count Increase
Fig. 6 Schematic diagram
about diffusion of
thermal and fast neutron
𝐿1 depends on the amounts of
hydrogen in porous rock
12 times